## Slide 1: Lab 2: Hexadecimal and Branching
J. Nelson Amaral

## Slide 2: What you need to do
Given a 32-bit word:
bbbb bbbb bbbb bbbb bbbb bbbb bbbb bbbb
if it is the binary code of a MIPS branch instruction
then
print the assembly of the instruction using the
following format (example):
beq $8, $9, 0x00400130
else
do nothing
Address of the branch
target instruction

## Slide 3: How do you know if it is the code of a MIPS Instruction?

## Slide 4: MIPS branch-instruction encodings

## Slide 5: Printing Format
beq $8, $9, 0x00400130
How is this 32-bit
value obtained?
Address of the branch
target instruction

## Slide 6: The input to disassembleBranch
$a0 contains the address of the assembly instruction.
$t0
0x0040 0100
$a0
Memory
0x0040 0108
0x0040 0104
0x0040 0100
0x0040 00fc
0x0040 01f8
Address
Content

## Slide 7: The input to disassembleBranch
$a0 contains the address of the assembly instruction.
0x1109000b
$t0
0x1109000b
0x0040 0100
$a0
Memory
0x0040 0108
0x0040 0104
0x0040 0100
0x0040 00fc
0x0040 01f8
Address
Content

## Slide 8
Value | Binary | Digit
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
Value | Binary | Digit
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | a
11 | 1011 | b
12 | 1100 | c
13 | 1101 | d
14 | 1110 | e
15 | 1111 | f
Hexadecimal
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 9: Manipulating the Offset
$a0 contains the address of the assembly instruction.
0x1109000b
$t0
0x1109000b
0x1109
000b
0000 0000 0000 1011
00
0000 0000 0000 00
0x0000 002c
sign extension
0x0040 0100
$a0
0x0040 0108
0x0040 0104
0x0040 0100
0x0040 00fc
0x0040 01f8
Memory
Address
Content

## Slide 10: Computing the Target
$a0 contains the address of the assembly instruction.
0x0040 0100
$a0
0x1109000b
$t0
0x1109000b
0x0000 002c
0
$t1
0x0040 0130
0x0040 0108
0x0040 0104
0x0040 0100
0x0040 00fc
0x0040 01f8
Memory
Address
Content
+
0x0000 0004

## Slide 11: Computing the Target
0
$t1
0x0040 0130
beq $8, $9, 0x00400130
How do we transform
this binary representation?
Into this sequence
of ASCII characters?

## Slide 12: ASCII Table

## Slide 13: ASCII Table

## Slide 14: Printing the Target
0
$t1
0x0040 0130
beq $8, $9, 0x00400130
0000 0000 0100 0000 0001 0011 0000
Convert into 0x?? (The ASCII code for ‘0’)