## Slide 1: Topic 6: Arrays, Pointers and Stack Frames
José Nelson Amaral
University of Alberta

## Slide 2: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
C code:
void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
Assumption:
v ⟷ $a0
k ⟷ $a1
temp ⟷ $t0
P-H p. 149

## Slide 3: C Sort Example
Intermediate code (6):
tB ← $a1 << 2
tB ← $a0 + tB
$t0 ← M[tB] tA ← M[tB+4]
M[tB] ← tA M[tB+4] ← $t0
Intermediate code (7):
$t1 ← $a1 << 2
$t1 ← $a0 + $t1
$t0 ← M[$t1] $t2 ← M[$t1+4]
M[$t1] ← $t2 M[$t1+4] ← $t0
Intermediate code (5):
tB ← k*4
tB ← v + tB
temp ← M[tB] tA ← M[tB+4]
M[tB] ← tA M[tB+4] ← temp
Intermediate code (4):
tB ← v + k*4
temp ← M[tB] tA ← M[tB + 4]
M[tB] ← tA M[tB + 4] ← temp
Intermediate code (3):
tB ← v + k*4
temp ← M[tB] tA ← M[v + (k+1)*4]
M[tB] ← tA M[v +(k+1)*4] ← temp
Intermediate code (2):
temp ← M[v + k*4] tA ← M[v + (k+1)*4]
M[v + k*4] ← tA M[v +(k+1)*4] ← temp
C code:
void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
P-H p. 149
Intermediate code (1):
temp ← M[v + k*4] M[v + k*4] ← M[v + (k+1)*4] M[v +(k+1)*4] ← temp
Intermediate code (1):
temp ← M[v + k*4] M[v + k*4] ← M[v + (k+1)*4] M[v +(k+1)*4] ← temp
Intermediate code (2):
temp ← M[v + k*4] tA ← M[v + (k+1)*4]
M[v + k*4] ← tA M[v +(k+1)*4] ← temp
Intermediate code (3):
tB ← v + k*4
temp ← M[tB] tA ← M[v + (k+1)*4]
M[tB] ← tA M[v +(k+1)*4] ← temp
Intermediate code (4):
tB ← v + k*4
temp ← M[tB] tA ← M[tB + 4]
M[tB] ← tA M[tB + 4] ← temp
Intermediate code (5):
tB ← k*4
tB ← v + tB
temp ← M[tB] tA ← M[tB+4]
M[tB] ← tA M[tB+4] ← temp
Intermediate code (6):
tB ← $a1 << 2
tB ← $a0 + tB
$t0 ← M[tB] tA ← M[tB+4]
M[tB] ← tA M[tB+4] ← $t0
Assumption:
v ⟷ $a0
k ⟷ $a1
temp ⟷ $t0

## Slide 4: The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4) =(address of v[k])
lw $t0, 0($t1) # $t0 = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0
jr $ra # return to calling routine
1
2
3
C code:
void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
P-H p. 150
Intermediate code (7):
$t1 ← $a1 << 2
$t1 ← $a0 + $t1
$t0 ← M[$t1] $t2 ← M[$t1+4]
M[$t1] ← t$t2 M[$t1+4] ← $t0
Assumption:
v ⟷ $a0
k ⟷ $a1
temp ⟷ $t0

## Slide 5: The Sort Procedure in C
Non-leaf (calls swap)
C code:
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1; j >= 0 && v[j] > v[j + 1]; j -= 1) {
  swap(v,j);
  }
  }
  }
Assumption:
v ⟷ $a0
n ⟷ $a1
i ⟷ $s0
j ⟷ $s1
P-H p. 151

## Slide 6: for loop template
Test
Loop Body
Increment
Initialization
Block after
the loop
C code:
  …
  for (i = 0; i < n; i += 1) {
  /* loop body */
  }
  /* Block After the loop */

## Slide 7: The Sort Procedure in C
C code:
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1; j >= 0 && v[j] > v[j + 1]; j -= 1) {
  swap(v,j);
  }
  }
  }
P-H p. 151
Intermediate code (1):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
  for (j = i – 1; j >= 0 && v[j] > v[j + 1]; j -= 1) {
  swap(v,j);
  }
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (2):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
if (v[j+1] >= v[j]) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Assumption:
v ⟷ $a0
n ⟷ $a1
i ⟷ $s0
j ⟷ $s1

## Slide 8
Intermediate code (2):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
if (v[j+1] >= v[j]) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (3):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tA ← v[j];
tB ← v[j+1];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (4):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tC ← v + 4*j
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (3):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tA ← v[j];
tB ← v[j+1];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Assumption:
v ⟷ $a0
n ⟷ $a1
i ⟷ $s0
j ⟷ $s1

## Slide 9
Intermediate code (4):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tC ← v + 4*j;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (5):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4*j;
tC ← v + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (6):
sort:
sA ← $a0;
sB ← $a1;
i ← 0;
for1tst:
if (i >= sB) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4*j;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← j;
  swap($a0,$a1);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (5):
sort:
i ← 0;
for1tst:
if (i >= n) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4*j;
tC ← v + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
  swap(v,j);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Assumption:
v ⟷ $a0
n ⟷ $a1
i ⟷ $s0
j ⟷ $s1

## Slide 10
Intermediate code (6):
sort:
sA ← $a0;
sB ← $a1;
i ← 0;
for1tst:
if (i >= sB) goto exit1;
j ← i-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4*j;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← j;
  swap($a0,$a1);
  j ← j -1;
  goto for2tst;
  exit2:
  i ← i+1;
  goto for1tst;
  exit1:
Intermediate code (7):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
j ← $s0-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4 * j;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← j;
  swap($a0,$a1);
  j ← j -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Intermediate code (7):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
j ← $s0-1;
for2tst:
if (j < 0) goto exit2;
tD ← 4 * j;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← j;
  swap($a0,$a1);
  j ← j -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Intermediate code (8):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
$s1 ← $s0-1;
for2tst:
if ($s1 < 0) goto exit2;
tD ← 4 * $s1;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC+4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Assumption:
v ⟷ $a0
n ⟷ $a1
i ⟷ $s0
j ⟷ $s1

## Slide 11
Intermediate code (8):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
$s1 ← $s0 - 1;
for2tst:
if ($s1 < 0) goto exit2;
tD ← 4 * $s1;
tC ← sA + tD;
tA ← M[tC];
tB ← M[tC + 4];
if (tB >= tA) goto exit2;
$a0 ← sA;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Intermediate code (9):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
$s1 ← $s0 - 1;
for2tst:
if ($s1 < 0) goto exit2;
$t1 ← 4 * $s1;
$t2 ← sA + $t1;
$t3 ← M[$t2];
$t4 ← M[$t2 + 4];
if ($t4 >= $t3) goto exit2;
$a0 ← sA;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Intermediate code (10):
sort:
$s2 ← $a0;
$s3 ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= $s3) goto exit1;
$s1 ← $s0 - 1;
for2tst:
if ($s1 < 0) goto exit2;
$t1 ← 4 * $s1;
$t2 ← $s2 + $t1;
$t3 ← M[$t2];
$t4 ← M[$t2 + 4];
if ($t4 >= $t3) goto exit2;
$a0 ← $s2;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:
Intermediate code (9):
sort:
sA ← $a0;
sB ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= sB) goto exit1;
$s1 ← $s0 - 1;
for2tst:
if ($s1 < 0) goto exit2;
$t1 ← 4 * $s1;
$t2 ← sA + $t1;
$t3 ← M[$t2];
$t4 ← M[$t2 + 4];
if ($t4 >= $t3) goto exit2;
$a0 ← sA;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:

## Slide 12
Intermediate code (10):
sort:
$s2 ← $a0;
$s3 ← $a1;
$s0 ← 0;
for1tst:
if ($s0 >= $s3) goto exit1;
$s1 ← $s0 - 1;
for2tst:
if ($s1 < 0) goto exit2;
$t1 ← 4 * $s1;
$t2 ← $s2 + $t1;
$t3 ← M[$t2];
$t4 ← M[$t2 + 4];
if ($t4 >= $t3) goto exit2;
$a0 ← $s2;
$a1 ← $s1;
  swap($a0,$a1);
  $s1 ← $s1 -1;
  goto for2tst;
  exit2:
  $s0 ← $s0 + 1;
  goto for1tst;
  exit1:

## Slide 13
Assembly Code:
sort:
move $s2, $a0 # $s2 ← $a0; $s2 ← v
move $s3, $a1 # $s3 ← $a1; $s3 ← n
move $s0, $0 # $s0 ← 0; i ← 0
for1tst:
bge $s0, $s3, exit1 # if ($s0 >= $s3) goto exit1; if i >= n goto exit1
addi $s1, $s0, -1 # $s1 ← $s0 - 1; j ← i - 1
for2tst:
blt $s1, $0, exit2 # if ($s1 < 0) goto exit2; if j<0 goto exit2
sll $t1, $s1, 2 # $t1 ← 4 * $s1; $t1 ← 4*j
add $t2, $s2, $t1 # $t2 ← $s2 + $t1; $t2 ← v + 4*j
lw $t3, 0($t2) # $t3 ← M[$t2]; $t3 ← v[j]
lw $t4, 4($t2) # $t4 ← M[$t2 + 4]; $t4 ← v[j+1]
bge $t4, $t3, exit2 # if ($t4 >= $t3) goto exit2; if v[j+1] >= v[j] goto exit2
move $a0, $s2 # $a0 ← $s2; 1st param. of swap ← v
move $a1, $s1 # $a1 ← $s1; 2nd param. Of swap ← j
  jal swap # swap($a0,$a1); swap(v,j)
  addi $s1, $s1, -1 # $s1 ← $s1 -1; j ← j-1
  j for2tst # goto for2tst; goto for2tst
  exit2:
  addi $s0, $s0, 1 # $s0 ← $s0 + 1; i ← i+1
  j for1tst # goto for1tst; goto for1tst
  exit1:
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 14
Assembly Code:
sort:
move $s2, $a0 # $s2 ← $a0; $s2 ← v
move $s3, $a1 # $s3 ← $a1; $s3 ← n
move $s0, $0 # $s0 ← 0; i ← 0
for1tst:
bge $s0, $s3, exit1 # if ($s0 >= $s3) goto exit1; if i >= n goto exit1
addi $s1, $s0, -1 # $s1 ← $s0 - 1; j ← i - 1
for2tst:
blt $s1, $0, exit2 # if ($s1 < 0) goto exit2; if j<0 goto exit2
sll $t1, $s1, 2 # $t1 ← 4 * $s1; $t1 ← 4*j
add $t2, $s2, $t1 # $t2 ← $s2 + $t1; $t2 ← v + 4*j
lw $t3, 0($t2) # $t3 ← M[$t2]; $t3 ← v[j]
lw $t4, 4($t2) # $t4 ← M[$t2 + 4]; $t4 ← v[j+1]
bge $t4, $t3, exit2 # if ($t4 >= $t3) goto exit2; if v[j+1] >= v[j] goto exit2
move $a0, $s2 # $a0 ← $s2; 1st param. of swap ← v
move $a1, $s1 # $a1 ← $s1; 2nd param. Of swap ← j
  jal swap # swap($a0,$a1); swap(v,j)
  addi $s1, $s1, -1 # $s1 ← $s1 -1; j ← j-1
  j for2tst # goto for2tst; goto for2tst
  exit2:
  addi $s0, $s0, 1 # $s0 ← $s0 + 1; i ← i+1
  j for1tst # goto for1tst; goto for1tst
  exit1:
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 15: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine
P-H p. 155
Assumption: v ← $a0
n ← $a1
i ← $s0
j ← $s1

## Slide 16: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux
See section 2.15 in CD for compiler optimizations.

## Slide 17: Effect of Language and Algorithm

## Slide 18: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 19: Arrays vs. Pointers
Array indexing:
P-H p. 157
pointer ← v
for(…){
reg ← M[pointer]
pointer = pointer+1
}
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2
array
$a0
i
$t0
for(…){
$t2 ← array+4×i
M[$t2] ← $zero
i = i+1
}
array
$a0
p
$t0
p ← array
$t2 ← &array[size]
for(…){
M[p] ← $zero
p = p+4
}
Pointer indexing:

## Slide 20: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers
P-H p. 157

## Slide 21: Example: Clearing an Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2
P-H pp. 157-160
add, addi, slt, sll: 1 cycle; sw: 5 cycles; bne: 2 cycles
Assume size is very large. Compute CPI. Which is faster? By how much?

## Slide 22: Example: Clearing an Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 1 loop1: sll $t1,$t0,2 # $t1 = i * 4 1 add $t2,$a0,$t1 # $t2 = 1 # &array[i] sw $zero, 0($t2) # array[i] = 05 addi $t0,$t0,1 # i = i + 1 1 slt $t3,$t0,$a1 # $t3 = 1 # (i < size) bne $t3,$zero,loop1 # if (…) 2 # goto loop1 | move $t0,$a0 # p = & array[0]1 sll $t1,$a1,2 # $t1 = size * 41 add $t2,$a0,$t1 # $t2 = 1 # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 5 addi $t0,$t0,4 # p = p + 4 1 slt $t3,$t0,$t2 # $t3 = 1 #(p<&array[size]) bne $t3,$zero,loop2 # if (…) 2 # goto loop2
P-H pp. 157-160
add, addi, slt, sll: 1 cycle; sw: 5 cycles; bne: 2 cycles
Assume size is very large. Compute CPI. Which is faster? By how much?

## Slide 23: Comparison of Array vs. Ptr
Array version requires shift to be inside loop
  It is part of index calculation for incremented i
  recalculate address in each iteration
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer
P-H p. 157

## Slide 24: Parameter Passing
What is the difference between passing a parameter by value and passing it by reference?

## Slide 25: The car.c program
#include <stdio.h>
#define STRINGLENGTH 20
typedef struct c_node{
int vehicleID;
char make[STRINGLENGTH];
char model[STRINGLENGTH];
int year;
int mileage;
double cost;
struct c_node *next;
} CarNode;
void ReadCar(CarNode *car);
void PrintCar(CarNode car);
main()
{
CarNode mycar;
ReadCar(&mycar);
PrintCar(mycar);
}
void ReadCar(CarNode *car)
{
car->vehicleID = 2;
strcpy(car->make,"DODGE");
strcpy(car->model,"STRATUS");
car->year = 1996;
car->mileage = 70000;
car->cost = 4,525.74;
}
void PrintCar(CarNode car)
{
printf("vehicleID: %d\n",car.vehicleID);
printf("make: %s\n",car.make);
printf("model: %s\n",car.model);
printf("year: %d\n",car.year);
printf("mileage: %d\n",car.mileage);
printf("cost: %f\n",car.cost);
}
Patt and Patel, pp. 419

## Slide 26: The car.c program
#define STRINGLENGTH 20
typedef struct c_node{
int vehicleID;
char make[STRINGLENGTH];
char model[STRINGLENGTH];
int year;
int mileage;
double cost;
struct c_node *next;
} CarNode;
vehicleID
make[20]
model[20]
year
mileage
cost
next
0
4
8
12
16
20
24
28
32
36
40
44
48
52
56
60
64

## Slide 27: The car.c program
#include <stdio.h>
#define STRINGLENGTH 20
typedef struct c_node{
int vehicleID;
char make[STRINGLENGTH];
char model[STRINGLENGTH];
int year;
int mileage;
double cost;
struct c_node *next;
} CarNode;
void ReadCar(CarNode *car);
void PrintCar(CarNode car);
main()
{
CarNode mycar;
ReadCar(&mycar);
PrintCar(mycar);
}
main:
subu $sp, 168
sw $ra, 84($sp)
.frame $sp, 168, $ra
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 88
jal ReadCar
# 27 PrintCar(mycar);
addu $t6, $sp, 88
move $t9, $sp
addu $t0, $t6, 72
L1:
lw $t8, 0($t6)
addu $t6, $t6, 12
sw $t8, 0($t9)
lw $t7, -8($t6)
addu $t9, $t9, 12
sw $t7, -8($t9)
lw $t8, -4($t6)
sw $t8, -4($t9)
bne $t6, $t0, L1
lw $a0, 0($sp)
lw $a1, 4($sp)
lw $a2, 8($sp)
lw $a3, 12($sp)
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 84($sp)
addu $sp, 168
j $ra

## Slide 28: The car.c program
main:
subu $sp, 168
sw $ra, 84($sp)
.frame $sp, 168, $ra
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 88
jal ReadCar
# 27 PrintCar(mycar);
addu $t6, $sp, 88
move $t9, $sp
addu $t0, $t6, 72
L1:
lw $t8, 0($t6)
addu $t6, $t6, 12
sw $t8, 0($t9)
lw $t7, -8($t6)
addu $t9, $t9, 12
sw $t7, -8($t9)
lw $t8, -4($t6)
sw $t8, -4($t9)
bne $t6, $t0, L1
lw $a0, 0($sp)
lw $a1, 4($sp)
lw $a2, 8($sp)
lw $a3, 12($sp)
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 84($sp)
addu $sp, 168
j $ra
next
cost
cost
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
make[0-3]
vehicleID
SP
00
04
08
12
16
20
24
28
32
36
40
44
48
52
56
60
64
68
72
76
80
84
88
92
180
184
188
96
100
104
108
112
116
120
124
128
132
136
140
144
148
152
156
160
164
168
172
176
$t9
$t6
$t0
$t8
$t7
vehicleID

## Slide 29: The car.c program
main:
subu $sp, 168
sw $ra, 84($sp)
.frame $sp, 168, $ra
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 88
jal ReadCar
# 27 PrintCar(mycar);
addu $t6, $sp, 88
move $t9, $sp
addu $t0, $t6, 72
L1:
lw $t8, 0($t6)
addu $t6, $t6, 12
sw $t8, 0($t9)
lw $t7, -8($t6)
addu $t9, $t9, 12
sw $t7, -8($t9)
lw $t8, -4($t6)
sw $t8, -4($t9)
bne $t6, $t0, L1
lw $a0, 0($sp)
lw $a1, 4($sp)
lw $a2, 8($sp)
lw $a3, 12($sp)
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 84($sp)
addu $sp, 168
j $ra
next
cost
cost
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
make[0-3]
vehicleID
SP
00
04
08
12
16
20
24
28
32
36
40
44
48
52
56
60
64
68
72
76
80
84
88
92
180
184
188
96
100
104
108
112
116
120
124
128
132
136
140
144
148
152
156
160
164
168
172
176
$t9
$t0
$t8
$t7
vehicleID
$t6
vehicleID
make[0-3]

## Slide 30: The car.c program
main:
subu $sp, 168
sw $ra, 84($sp)
.frame $sp, 168, $ra
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 88
jal ReadCar
# 27 PrintCar(mycar);
addu $t6, $sp, 88
move $t9, $sp
addu $t0, $t6, 72
L1: # loop copies 3 words
lw $t8, 0($t6)
addu $t6, $t6, 12
sw $t8, 0($t9)
lw $t7, -8($t6)
addu $t9, $t9, 12
sw $t7, -8($t9)
lw $t8, -4($t6)
sw $t8, -4($t9)
bne $t6, $t0, L1
lw $a0, 0($sp)
lw $a1, 4($sp)
lw $a2, 8($sp)
lw $a3, 12($sp)
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 84($sp)
addu $sp, 168
j $ra
next
cost
cost
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
make[0-3]
vehicleID
SP
00
04
08
12
16
20
24
28
32
36
40
44
48
52
56
60
64
68
72
76
80
84
88
92
180
184
188
96
100
104
108
112
116
120
124
128
132
136
140
144
148
152
156
160
164
168
172
176
$t0
$t8
$t7
vehicleID
$t6
vehicleID
make[0-3]
$t9
make[0-3]
make[4-7]
make[4-7]

## Slide 31: The car.c program
next
cost2
cost1
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
cost2
cost1
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
make[0-3]
make[0-3]
vehicleID
SP
00
04
08
12
16
20
24
28
32
36
40
44
48
52
56
60
64
68
72
76
80
84
88
92
180
184
188
96
100
104
108
112
116
120
124
128
132
136
140
144
148
152
156
160
164
168
172
176
vehicleID
next
$a0
vehicleID
$a1
make[0-3]
$a2
make[4-7]
$a3
make[8-11]
main:
subu $sp, 168
sw $ra, 84($sp)
.frame $sp, 168, $ra
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 88
jal ReadCar
# 27 PrintCar(mycar);
addu $t6, $sp, 88
move $t9, $sp
addu $t0, $t6, 72
L1: # loop copies 3 words
lw $t8, 0($t6)
addu $t6, $t6, 12
sw $t8, 0($t9)
lw $t7, -8($t6)
addu $t9, $t9, 12
sw $t7, -8($t9)
lw $t8, -4($t6)
sw $t8, -4($t9)
bne $t6, $t0, L1
lw $a0, 0($sp)
lw $a1, 4($sp)
lw $a2, 8($sp)
lw $a3, 12($sp)
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 84($sp)
addu $sp, 168
j $ra

## Slide 32: The car.c program
# 42 void PrintCar(CarNode car)
# 43 {
PrintCar:
subu $sp, 32
sw $ra, 28($sp)
sw $a0, 32($sp)
sw $a1, 36($sp)
sw $a2, 40($sp)
sw $a3, 44($sp)
# 44 printf("vehicleID: %d\n",car.vehicleID);
la $a0, string13
lw $a1, 32($sp)
jal printf
# 45 printf("make: %s\n",car.make);
la $a0, string14
addu $a1, $sp, 32
addu $a1, $a1, 4
jal printf
# 46 printf("model: %s\n",car.model);
la $a0, string15
addu $a1, $sp, 32
addu $a1, $a1, 24
jal printf
# 47 printf("year: %d\n",car.year);
la $a0, string16
lw $a1, 76($sp)
jal printf
next
cost2
cost1
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
cost2
cost1
mileage
year
model[16-19]
model[12-15]
model[8-11]
model[4-7]
model[0-3]
make[16-19]
make[12-15]
make[8-11]
make[4-7]
make[0-3]
make[0-3]
vehicleID
SP
00
04
08
12
16
20
24
28
32
36
40
44
48
52
56
60
64
68
72
76
80
84
88
92
180
184
188
96
100
104
108
112
116
120
124
128
132
136
140
144
148
152
156
160
164
168
172
176
vehicleID
next
$a0
vehicleID
$a1
make[0-3]
$a2
make[4-7]
$a3
make[8-11]

## Slide 33: Why so much copying?
The program car.c passes the datastructure CarNode
to the PrintCar function by value.
A copy of each byte of CarNode must be made in the
stack for each call of the function PrintCar.
We could, instead have passed the address of the copy
of CarNode that we already had in the stack.

## Slide 34: The car2.c Program
#include <stdio.h>
#define STRINGLENGTH 20
typedef struct c_node{
int vehicleID;
char make[STRINGLENGTH];
char model[STRINGLENGTH];
int year;
int mileage;
double cost;
struct c_node *next;
} CarNode;
void ReadCar(CarNode *car);
void PrintCar(CarNode *car);
main()
{
CarNode mycar;
ReadCar(&mycar);
PrintCar(&mycar);
}
void ReadCar(CarNode car)
{
car->vehicleID = 2;
strcpy(car->make,"DODGE");
strcpy(car->model,"STRATUS");
car->year = 1996;
car->mileage = 70000;
car->cost = 4,525.74;
}
void PrintCar(CarNode car)
{
printf("vehicleID: %d\n",car->vehicleID);
printf("make: %s\n",car->make);
printf("model: %s\n",car->model);
printf("year: %d\n",car->year);
printf("mileage: %d\n",car->mileage);
printf("cost: %f\n",car->cost);
}

## Slide 35
car-O0.s
car2-O0.s
#include <stdio.h>
#define STRINGLENGTH 20
typedef struct c_node{
int vehicleID;
char make[STRINGLENGTH];
char model[STRINGLENGTH];
int year;
int mileage;
double cost;
struct c_node *next;
} CarNode;
void ReadCar(CarNode *car);
void PrintCar(CarNode *car);
main()
{
CarNode mycar;
ReadCar(&mycar);
PrintCar(&mycar);
}
main:
subu $sp, 112
sw $ra, 28($sp)
# 23 CarNode mycar;
# 25 ReadCar(&mycar);
addu $a0, $sp, 32
jal ReadCar
# 27 PrintCar(&mycar);
addu $a0, $sp, 32
jal PrintCar
# 28 }
move $v0, $zero
lw $ra, 28($sp)
addu $sp, 112
j $ra

## Slide 36: Quiz #1
predecessors and successors are two vectors of unsigned integers.
Assume that:
predecessors’ first element is stored at $fp-64
successors’ first element is stored at $fp-32
Where $fp points to the top of the stack frame of the current procedure.
Write a sequence of assembly instructions that executes the following
C statement:
successors[5] = predecessors[7];

## Slide 37: Quiz #1 - Solution
predecessors and successors are two vectors of unsigned integers.
predecessors’ first element is stored at $fp-64
successors’ first element is stored at $fp-32
$t0 ← M[$fp-64+4*7]
M[$fp-32+4*5] ← $t0
----------------
$t0 ← M[$fp-36]
M[$fp-12] ← $t0
-------------
lw $t0, -36($fp)
sw $t0, -12($fp)

## Slide 38: Quiz #1 - Solution
predecessors and successors are two vectors of unsigned integers.
predecessors’ first element is stored at $fp-64
successors’ first element is stored at $fp-32
successors[5] = predecessors[7];
$t0 ← predecessors[7];
successors[5] ← $t0;
$t1 ← Addr(predecessor[7]);
$t0 ← M[$t1];
$t2 ← Addr(successors[5]);
M[$t2] ← $t0;
$t1 ← $fp-64+7*4
$t0 ← M[$t1];
$t2 ← $fp-32+5*4
M[$t2] ← $t0;
lw $t0, -36($fp)
sw $t0, -12($fp)
$t1 ← $fp-36
$t0 ← M[$t1];
$t2 ← $fp-12
M[$t2] ← $t0;
$t1 ← $fp-36
$t0 ← M[$fp-36];
$t2 ← $fp-12
M[$fp-12] ← $t0;
$t0 ← M[$fp-36];
M[$fp-12] ← $t0;

## Slide 39: Quiz #2
names is an array of pointers to strings.
Each position of names contains a pointer to a
null-terminated string.
Assume that the first element of names is stored in
the memory position $sp+16.
Write a sequence of MIPS assembly instructions
that counts the number of characters in the string
whose pointer is at names[7].

## Slide 40: Quiz #2
names is an array of pointers to strings.
Each position of names contains a pointer to a null terminated string.
Assume that the first element of names is stored in the memory position $fp-48.
Write a sequence of MIPS assembly instructions that counts the
number of characters in the string whose pointer is at names[7].
count = 0;
c = names[7];
while (*c != 0)
{
count = count+1;
c = c+1;
}
$t0 ← 0;
$t1 ← Address(names[7]);
$t2 ← M[$t1];
while (M[$t2] != 0)
{
$t0 = $t0+1;
$t2 = $t2+1;
}
$t0 ← 0;
$t2 ← names[7];
while ( M[$t2] != 0)
{
$t0 = $t0+1;
$t2 = $t2+1;
}
$t0 ← 0;
$t1 ← $fp-48+7*4
$t2 ← M[$t1];
while (M[$t2] != 0)
{
$t0 = $t0+1;
$t2 = $t2+1;
}

## Slide 41
$t0 ← 0;
$t1 ← $fp-48+7*4
$t2 ← M[$t1];
while (M[$t2] != 0)
{
$t0 = $t0+1;
$t2 = $t2+1;
}
add $t0, $zero, $zero
lw $t2, -20($fp)
lb $t3,0($t2)
beq $t3, $zero, done
addi $t0, $t0, 1
addi $t2, $t2, 1
j loop;
done:
loop:
$t0 ← 0;
$t2 ← M[$fp-20];
while (M[$t2] != 0)
{
$t0 = $t0+1;
$t2 = $t2+1;
}
Quiz #2
names is an array of pointers to strings.
Each position of names contains a pointer to a null terminated string.
Assume that the first element of names is stored in the memory position $fp-48.
Write a sequence of MIPS assembly instructions that counts the
number of characters in the string whose pointer is at names[7].

## Slide 42: Quiz #2 – Alternative Solution
names is an array of pointers to strings.
Each position of names contains a pointer to a null terminated string.
Assume that the first element of names is stored in the memory position $fp-48.
Write a sequence of MIPS assembly instructions that counts the
number of characters in the string whose pointer is at names[7].
count = 0;
c = names[7];
while (*c != 0)
{
count = count+1;
c = c+1;
}
Previous Solution:
count = 0;
c = names[7];
count = c;
while (*c != 0)
{
c = c+1;
}
count = c-count;
Alternative Solution:

## Slide 43: The meaning of *p
1 void foo(int *p, int x)
2 {
…
25 *p = x;
…
x = *p;
}
What is the meaning of the statement in line 25
of this C program?
0x10001010
0x10001014
0x10001018
0x10001000
0x10001004
0x10001008
0x1000100C
p
0x10001008
x
42
What does p contain?
What does x contain?
A memory address
An integer value
What action the program should do to execute
line 25?
Store the value of x in the memory
location whose address is in p.
42
What MIPS assembly instruction(s)
are needed to execute line 25?
sw $a1, 0($a0) # 0($a0)  $a1

## Slide 44: The meaning of *p
1 void foo(int *p, int x)
2 {
…
25 *p = x;
…
x = *p;
}
0x10001010
0x10001014
0x10001018
0x10001000
0x10001004
0x10001008
0x1000100C
p
0x10001008
x
42
What action the program should do to execute
line 30?
Load the value from the memory
location whose address is in p.
74
What MIPS assembly instruction(s)
are needed to execute line 30?
lw $a1, 0($a0) # $a1  0($a0)
74

## Slide 45: The meaning of *p
1 void foo(…)
2 {
3 int *p;
4 int x;
….
25 *p = x;
…
x = *p;
}
0x1000004
$sp
0x10000010
$fp
Now p and x are in memory in the local stack
frame. Assume that:
p ↔ $fp-4
x ↔ $fp-12
1. Load the address in p into a register (say $s0).
Now, what actions are needed to execute line 25?
0x10001010
0x10001014
0x10001018
0x10001000
0x10001004
0x10001008
0x1000100C
0x10000010
0x10000014
0x10000018
0x10000000
0x10000004
0x10000008
0x1000000C
…
fp
sp
p
x
0x10001008
42
$s0
0x10001008
2. Load the value of x into a register (say $s1).
$s1
42
3. Store the value in $s1 into the address in $s0.
42
What MIPS assembly instruction(s)
are needed to execute line 25?
lw $s0, -4($fp) # $s0  p
lw $s1, -12($fp) # $s1  x
sw $s1, 0($s0) # *p  x

## Slide 46: The meaning of *p
1 void foo(…)
2 {
3 int *p;
4 int x;
…
25 *p = x;
…
x = *p;
}
0x1000004
$sp
0x10000010
$fp
Now p and x are in memory in the local stack
frame. Assume that:
p ↔ $fp-4
x ↔ $fp-12
1. Load the address in p into a register (say $s0).
Now, what actions are needed to execute line 30?
0x10001010
0x10001014
0x10001018
0x10001000
0x10001004
0x10001008
0x1000100C
0x10000010
0x10000014
0x10000018
0x10000000
0x10000004
0x10000008
0x1000000C
…
fp
sp
p
x
0x10001008
42
$s0
0x10001008
2. Load the value of the memory whose address is in $s0
into a register (say $t1).
$t1
74
3. Store the value in $t1 into the address of x.
74
What MIPS assembly instruction(s)
are needed to execute line 30?
lw $s0, -4($fp) # $s0  p
lw $t1, 0($s0) # $s1  x
sw $t1, -12($fp) # x  *p
74
$s1
42
What is the difference
between the address “in p”
and the address “of p”?

## Slide 47: Quiz #3
Consider the following C function:
Write the MIPS assembly code for the statement immediately before the call to printf.
Assume:
temp ⟷ $s0
node ⟷ $s1
int ReadGraph(FILE *input_file, unsigned int **successors, char ***names)
{
unsigned int temp = 0;
unsigned int node = 0;
/* Input code that uses input_file removed for clarity */
(*successors)[node] = temp;
printf(“name = %d\n”,*names[node]);
}

## Slide 48: Quiz #3 - Solution
int ReadGraph(FILE *input_file, unisgned int **successors, char ***names)
{
unsigned int temp = 0;
unsigned int node;
(*successors)[node] = temp;
printf(“name = %d\n”,*names[node]);
}
(*successors)[node] ← temp;
0($a1)[node] ← temp;
$t0 ← 0($a1)
$t1 ← Address($t0[node])
0($t1) ← temp;
$t0 ← 0($a1)
$t0[node] ← temp;
$t0 ← 0($a1)
$t1 ← $t0 + 4*node
0($t1) ← temp;
lw $t0, 0($a1)
sll $t2, $s1, 2
add $t1, $t0, $t2
sw $s0, 0($t1)
temp ← $s0
node ← $s1
$t0 ← 0($a1)
$t2 ← 4*node
$t1 ← $t0 + $t2
0($t1) ← temp;
0($a1) represents a load from the address
in $a1 with offset 0.
$t0 contains the base address of
an array of pointers.
Here 0($t1) is a
store into the
address in $t1 with
offset of zero

## Slide 49: Quiz #4
Consider the following C function:
Write the MIPS assembly code to initialize the value of $a1 in
the function call to printf.
Assume:
node ⟷ $s1
names ⟷ $a2
int ReadGraph(FILE *input_file, unsigned int **successors, char ***names)
{
unsigned int temp;
unsigned int node;
(*successors)[node] = temp;
printf(“name = %s\n”,(*names)[node]);
}

## Slide 50: How did we ended up with ***names ?
A
d
a
m
\0
J
a
m
e
\0
s
C
e
c
i
\0
l
y
M
u
r
r
\0
a
y

## Slide 51: How did we ended up with ***names ?
A
d
a
m
\0
J
a
m
e
\0
s
C
e
c
i
\0
l
y
M
u
r
r
\0
a
y
names
*names
**names
***names ≡ **names[0]
*(**names+1) ≡ **names[1]
*(**names+2) ≡ **names[2]
*(**names+3) ≡ **names[3]

## Slide 52
int ReadGraph(FILE *input_file, unisgned int **successors, char ***names)
{
…
printf(“..”,(*names)[node]);
}
lw $t0, 0($a2) # $t0 ← *names
$a2
$t3
lw $t0, 0($a2) # $t0 ← *names
sll $t2, $s1, 2 # $t2 ← 4×node
add $t3, $t0, $t2 # $t3 ← (*names) + 4×node
$t0
A
d
a
m
\0
J
a
m
e
\0
s
C
e
c
i
\0
l
y
M
u
r
r
\0
a
y
node ⟷ $s1
names ⟷ $a2
Animation assumes that node = 2.

## Slide 53
int ReadGraph(FILE *input_file, unsigned int **successors, char ***names)
{
…
printf(“..”,(*names)[node]);
}
A
d
a
m
\0
J
a
m
e
\0
s
C
e
c
i
\0
l
y
$a2
lw $t0, 0($a2) # $t0 ← *names
sll $t2, $s1, 2 # $t2 ← 4×node
add $t3, $t0, $t2 # $t3 ← (*names) + 4×node
lw $a1, 0(t3) # $a1 ← (*names)[node]
$t3
$a1
$t0
M
u
r
r
\0
a
y
node  $s1
names  $a2
Animation assumes that node = 2.

## Slide 54
int ReadGraph(FILE *input_file, unsigned int **successors, char ***names)
{
unsigned int temp;
unsigned int node;
(*successors)[node] = temp;
printf(“name = %s\n”,(*names)[node]);
}
lw $t0, 0($a2) # $t0 ← *names
sll $t2, $s1, 2 # $t2 ← 4×node
add $t3, $t1, $t2 # $t3 ← (*names) + 4×node
lw $a1, 0(t3) # $a1 ← (*names)[node]

## Slide 55: Quiz #7
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
⟨ind⟩
Stack
⟨apple⟩
⟨ptr⟩
$sp
0
4
8
Next we will
simulate each
line of the C code.

## Slide 56: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
⟨apple⟩
⟨ptr⟩
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 57: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
⟨apple⟩
⟨ptr⟩
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 58: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
⟨apple⟩
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 59: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
⟨apple⟩
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 60: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
123
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 61: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+4
Stack
123
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 62: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+8
Stack
123
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 63: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+8
Stack
123
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 64: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+8
Stack
124
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 65: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+8
Stack
124
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1

## Slide 66: Quiz #7
1 #include <stdio.h>
2 main()
3 {
4 int apple;
5 int *ptr;
6 int **ind;
7 ind = &ptr;
8 *ind = &apple;
9 **ind = 123;
10 ind++;
11 *ptr++;
12 apple++;
13 printf(“%x %x %d\n”, ind, ptr, apple);
14 }
$sp+8
Stack
125
$sp+8
$sp
0
4
8
Write MIPS assembly for the
following program.
Assume that:
apple ↔ $sp+8
ptr ↔ $sp+4
ind ↔ $sp+0
# 7 ind = &ptr;
addi $t0, $sp, 4 # $t0 ← &ptr
sw $t0, 0($sp) # ind ← &ptr
# 8 *ind = &apple;
lw $t0, 0($sp) # $t0 ← ind
addi $t1, $sp,8 # $t1 ← &apple
sw $t1, 0($t0) # *ind ← &apple
# 9 **ind = 123;
addi $t3,$zero,123
lw $t4, 0($sp) # $t4 ← ind
lw $t5, 0($t4) # $t5 ← *ind
sw $t3, 0($t5) # **ind ← 123
# 10 ind++;
lw $t0, 0($sp) # $t0 ← ind
addi $t0, $t0, 4 # $t0 ← ind + 4
sw $t0, 0($sp) # ind ← ind + 4
# 11 *ptr++;
lw $t6, 4($sp) # $t6 ← ptr
lw $t7, 0($t6) # $t7 ← *ptr
addi $t7, $t7, 1 # $t7 ← (*ptr) + 1
sw $t7, 0($t6) # *ptr ← (*ptr) + 1
# 12 apple++;
lw $t8, 8(sp) # $t8 ← apple
addi $t8, $t8, 1 # $t8 ← apple + 1
sw $t8, 8(sp) # apple ← apple + 1