## Slide 1: Topic 4
Procedure Calling
(Modified by J. Nelson Amaral)

## Slide 2: Procedure calls
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
caller
callee
caller
callee
return address
must remember return address
must return to correct return address
return address

## Slide 3: Problem
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
write return address into $ra
In MIPS there is a single register,
$ra, to store the return address.
overwrite return
address into $ra
return to wrong address
return to correct
address

## Slide 4: Solution
We need to save the value of $ra somewhere.
Where?
Into the stack.

## Slide 5: What goes into the stack
The value of the register $ra
(if the function calls another function).
Any register that is modified by the function.
Any local variables that need memory storage.
The value of the register $fp.

## Slide 6: Where is the top of the Stack?
MIPS has a special register called stack pointer ($sp)
$sp always contains the address of the top of the stack.

## Slide 7: Saving Register into the Stack
$sp
Memory
↑ High Address
↓ Low Address
0x1000 4004
$ra
Problem: a subroutine will write on $a0
and call another subroutine.
Must save values of $a0, $fp and $ra into the stack.
0x1000 2000
$sp
How do we make room in the stack for these
three registers?
The stack grows towards lower memory addresses.
0x0000 0003
$a0
0x1000 200C
$fp

## Slide 8: Saving Register into the Stack
0x0000 0003
$a0
0x1000 4004
$ra
Problem: a subroutine will write on $a0
and call another subroutine.
Must save values of $a0 and $ra into the stack.
0x1000 2000
$sp
How do we make room in the stack for these
two registers?
The stack grows towards lower memory addresses.
$sp
Memory
↑ High Address
↓ Low Address
We need to decrement the value of $sp by 12.
0x1000 1FF4
How do we actually “save” $a0, $ra and $fp?
Write their values, using the sw instruction,
to the stack.
0x1000 200C
0x0000 0003
0x1000 200C
$fp
0x1000 4004

## Slide 9: Solution
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
write return address into $ra
In MIPS there is a single register,
$ra, to store the return address.
safe to overwrite return
address into $ra
return to correct address
save $ra into stack
restore $ra from stack
return to correct
address

## Slide 10: Saving Register into the Stack
0x0000 01F7
$a0
0x1000 41F8
$ra
How do we “restore” the values of $a0, $fp, and $ra?
0x1000 2000
$sp
Do we need to do anything to the value of $sp?
Now the procedure has completed its execution and
it it time to return to the caller.
$sp
Memory
↑ High Address
↓ Low Address
Yes, we need to increment the value of $sp by 12.
0x1000 1FF4
Read their values, using the lw instruction,
from the stack.
0x0000 0003
0x1000 4004
0x0000 0003
0x1000 4004
0x0000 0003
0x1000 4004
0x1000 2004
$fp
0x1000 200C
0x1000 200C
0x1000 200C

## Slide 11: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
P-H p. 120

## Slide 12: Optimization
It would be wasteful if every callee had to save/restore every register that it uses.
  The callee might be saving/restoring registers that are not in use by the caller at the call point.
Register context calling convention:
  Some registers are reserved for use by caller
  Others are reserved for callee

## Slide 13: Concept of Liveness
A register is live if it contains a value that may be used in the future.
A register is dead if it contains a value that will never be used in the future.

## Slide 14: Calling Convention
foo{
…
bar();
….
}
bar(){
….
}
Save live caller-saved registers.
Save callee-saved registers that are
written by the callee.
Restore saved callee-saved registers.
Restore live caller-saved registers.

## Slide 15: Register Saving Convention
To avoid saving and restoring dead registers, MIPS
adopts the following software convention:
These names indicates which procedure (the caller or the callee)
is responsible for preserving the value stored in the register
at the procedure boundary.
P-H p. 118
Registers $t0-$t9 are not preserved by the callee on a
procedure call.
Registers $s0-$s7 must be preserved on a procedure call.
Registers $t0-$t9 are the caller-saved registers
Registers $s0-s7 are callee-saved registers.

## Slide 16: Registers Used for Procedure Calls
$a0-$a3: four argument registers in which to pass parameters
$v0-$v1: two value registers in which to return values
$ra: one return address register to return to the point of origin
Pat.-Hen. pp. 132

## Slide 17: Register Usage Convention
P-H p. B-24

## Slide 18: Register Usage Convention
P-H p. B-24

## Slide 19: Register Usage Convention
P-H p. B-24

## Slide 20: Register Usage Convention
P-H p. B-24

## Slide 21: Register Usage Convention
P-H p. B-24

## Slide 22: Register Usage Convention
P-H p. B-24

## Slide 23: Register Usage Convention
P-H p. B-24

## Slide 24: Register Usage Convention
P-H p. B-24

## Slide 25: Register Usage Convention
P-H p. B-24

## Slide 26: Register Usage Convention
P-H p. B-24

## Slide 27: Register Usage Convention
P-H p. B-24

## Slide 28: Frame Pointer
Save $fp
Some procedures may change $sp during its execution. Then:
Move $fp
to first position of frame
Always use $fp to access stack
Restore $fp

## Slide 29: Frame Pointer (Example)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
0x1000101C
callee’s
frame

## Slide 30: Frame Pointer (Example – at begin)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
0x1000101C
callee’s
frame
sw $fp, 0($sp)
move $fp, $sp
add $sp, $sp, -12
sw $s0, -4($fp)
∙∙∙
addi $sp, $sp, -4
0xFADEF100
0xABCDEF00
0x12345678

## Slide 31: Frame Pointer (Example - at end)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
callee’s
frame
addi $sp, $sp, 16
lw $s0, -4(fp)
∙∙∙
lw $fp, 0($fp)
0x1000101C
0xFADEF100
0x1000101C
0xFADEF100
0xABCDEF00
0x12345678
0xABCDEF00
0x12345678

## Slide 32
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Execute callee
Place result in return register
add $v0, $zero, $t5
Return control to caller
jr $ra
Not using stack

## Slide 33
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, 0($sp)
sw $s0, 4($sp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, 0($sp)
lw $s0, 4($sp)
Return control to caller
jr $ra
Using stack
no $fp

## Slide 34
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Save $fp
addi $sp, $sp, -4
sw $fp, 0($sp)
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, -4($fp)
sw $s0, -8($fp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, -4($fp)
lw $s0, -8($fp)
lw $fp, 0($fp)
Restore stack pointer
addi $sp, $sp, 12
Return control to caller
jr $ra
Using stack
with $fp

## Slide 35
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Save $fp
addi $sp, $sp, -4
sw $fp, 0($sp)
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, -4($fp)
sw $s0, -8($fp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, -4($fp)
lw $s0, -8($fp)
lw $fp, 0($fp)
Restore stack pointer
addi $sp, $sp, 12
Return control to caller
jr $ra
Save caller-saved registers
addi $sp, $sp, -4
sw $t0, -8($fp)
Caller Acquire storage
Restore caller-saved registers
lw $t0, -8($fp)
addi $sp, 4
Restore stack pointer

## Slide 36: Procedure Call Instructions
jal ProcedureLabel
jr $ra
P-H p. 113
Procedure call: jump and link
Procedure return: jump register
  Address of following instruction put in $ra
  Jumps to target address
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 37: Branch and Link
BGEZAL: Branch on greater than or equal to zero
and save return address in $ra.
Example:
bgezal $s0, offset
Operation:
PC ← PC + 4
if $s0 ≥ 0
$ra ← PC
PC ← PC + offset<<2
Binary representation:
0000 01ss sss1 0001 iiii iiii iiii iiii
link bit:
0: bgez
1: bgezal

## Slide 38: Branch and Link
BLTZAL: Branch on less than zero
and save return address in $ra.
Example:
bltzal $s0, offset
Operation:
PC ← PC + 4
if $s0 < 0
$ra ← PC
PC ← PC + offset<<2
Binary representation:
0000 01ss sss1 0000 iiii iiii iiii iiii
link bit:
0: bgez
1: bgezal

## Slide 39: Leaf Procedure Example
Have to save $s0 on stack
C code:
int leaf_example (int g, h, i, j)
{
int f;
f = (g+h) - (i+j);
return f;
}
P-H p. 114
Assumption:
g ↔ $a0
h ↔ $a1
i ↔ $a2
j ↔ $a3
f ↔ $s0
result ↔ $v0

## Slide 40: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j)
{
int f;
f = (g+h) - (i+j);
return f;
}
P-H p. 114
Assumption:
g ↔ $a0
h ↔ $a1
i ↔ $a2
j ↔ $a3
f ↔ $s0
result ↔ $v0
add $t0, $a0, $a1 # $t0 ← g+h
add $t1, $a2, $a3 # $t1 ← i+j
sub $s0, $t0, $t1 # f ← (g+h) – (i+j)
add $v0, $s0, $zero # $v0 ← f
$s0 is a callee-saved register, therefore we need to save/restore it
$sp
↑ High Address
↓ Low Address
Memory
sw $s0, 0($sp) # save $s0
addi $sp, $sp, -4 # grow stack
lw $s0, 0($sp) # restore $s0
addi $sp, $sp, 4 # shrink stack
leaf_example:
0x0000 0004
0x0000 0004
jr $ra # return

## Slide 41: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to:
  Save on the stack:
    Its return address
    Arguments and temporaries needed after the call
  Restore values from the stack after the call
P-H p. 116

## Slide 42: Calling Itself
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
P-H p. 117

## Slide 43: The Factorial Function
save ($ra,$a0)
if (n < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
$v0 ← fact($a0);
restore ($ra,$a0);
tA ← n * $v0;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
$v0 ← fact($a0);
tA ← n * $v0;
restore $ra;
return(tA);
}
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
save $ra
if (n < 1){
restore $ra;
return(1);
}
else{
tA ← n * fact(n-1);
restore $ra;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
tA ← n * fact($a0);
restore $ra;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
tA ← n * fact(n-1);
restore $ra;
return(tA);
}
save ($ra,$a0)
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
restore ($ra,$a0);
tA ← $a0 * $v0;
return(tA);
}

## Slide 44: The Factorial Function
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}
save ($ra,$a0)
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
restore ($ra,$a0);
$v0 ← $a0 * $v0;
return($v0);
}
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
$sp ← $sp+8;
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}

## Slide 45: Linking a Recursive Procedure
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slt $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n < 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact: # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
$sp ← $sp+8;
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
P-H pp. 117-118
P-H pp. 117-118

## Slide 46: Linking a Recursive Procedure
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
add $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
P-H pp. 117-118

## Slide 47: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
$a0
Processor
0x1000 2000
$sp
$ra
$sp
Memory
↑ High Address
↓ Low Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 48: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 2000
$sp
$ra
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 49: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
$sp
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 50: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n <≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 51: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 52: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 53: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 54: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 55: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
0x1000 4004
3
$sp
Memory
↑ High Address
↓ Low Address
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 56: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 57: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 58: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 59: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
↓ Low Address

## Slide 60: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 61: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 62: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
↓ Low Address

## Slide 63: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 64: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 65: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0
$sp

## Slide 66: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 67: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 68: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 69: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0
$sp

## Slide 70: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 71: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 72: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 73: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0

## Slide 74: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 75: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 76: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 77: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 78: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 79: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
6
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 80: Example fact(3)
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
6
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 81: Other Data Stored in the Stack
$sp
↑ High Address
↓ Low Address
$fp
Before procedure
call
$sp
↑ High Address
↓ Low Address
$fp
After procedure
call
$sp
↑ High Address
↓ Low Address
$fp
During procedure
call
Saved argument
registers
Saved return reg.
Saved
registers
Local arrays
and structures
Patt.-Hen. pp 139
P-H p. 119

## Slide 82: Instructions to maniputate characters (Bytes)
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword
P-H p. 123

## Slide 83: String Copy Example
C code (naïve):
  Null-terminated string
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
P-H p. 124

## Slide 84: String Copy Example
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
P-H p. 124
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if (y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if (y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;

## Slide 85: How do I know by how much to multiply the index of an array?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Look at the size of each element of the array!
int X[100];
address(X[i]) = X + 4×i;
char S[100];
address(S[j]) = S + j;
base of X
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of S
address(F[k]) = F + 8×k;
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of F
double F[100];

## Slide 86: You can create an array of anything.
C code:
…
struct city {
int DistanceFromCoast;
int Population;
char Subway;
char RingRoad;
};
struct city T[150];
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of T
address(T[i]) = T + 10×k;

## Slide 87: String Copy Example
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
P-H p. 124
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if (y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$sp ← $sp - 4
M[$sp] ← $s0
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: $s0 ← M[$sp]
$sp ← $sp + 4;
return;
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if (y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
<save registers>
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: <restore registers>
return;

## Slide 88: String Copy Example
MIPS assembly:
strcpy:
addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i ← 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 ← y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] ← y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i ← i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
P-H p. 125
Intermediate Code:
strcpy:
$sp ← $sp - 4
M[$sp] ← $s0
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if ($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: $s0 ← M[$sp]
$sp ← $sp + 4;
return;